| CERTIFICATE OF ANALYSIS |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Common Name |  | Hina AG |  |  |  |  |  |  |  |
| Product Code Category |  | HIN/17/46/B Base |  |  |  |  |  |  |  |
| Method of Production |  | Mixture of various Aromatic Chemicals , Essential Oils and Absolutes |  |  |  |  |  |  |  |
| Color and Appearance |  | Brownish yellow mobile liquid. |  |  |  |  |  |
| Odor |  | Extremely tenacious with a delightful, warm spiciness and Balsamic floral undertone. |  |  |  |  |
| Country of Origin |  | India |  |  |  |  |  |  |  |  |
| Packing |  | 1 Kg, 5kg Aluminum Bottles, non-standard packing on request. |  |  |  |
| Main ingredients |  | Ketone 101, Beta Ionone , Methyl Phenyl Acetate, Benzyl Phenyl Acetate. |  |  |  |  |  |
| Density 200C |  | 1.0256 |  |  |  |  |  |  |  |  |
| Refractive Index 200C |  | 1.5195 |  |  |  |  |  |  |  |  |
| Optical Rotation |  | (-)4.618 |  |  |  |  |  |
| Flash Point |  | Not determined, estimated above 800 C . |  |  |  |  |  |
| Solubility |  | Insoluble in water, soluble in oils & alcohol |  |  |  |
| Stability |  | 24 months shelf life if stored properly |  |  |  |  |  |
| Storage |  | To be kept in closed container, in a dark, fresh & dry place |  |  |  |
| Safety |  | Harmful if swallowed. Avoid contact with eyes. |  |  |  |  |
| GC Profile |  | Attached |  |  |  |  |  |  |  |  |

Manufacturer						BMV Fragrances Pvt Ltd

J – 44, 45 & 46 Surajpur Industrial Area , Site V ,

Kasna, Greater Noida  ( UP )   India - 201308

Tel  No : +91 - 8800397839 / 8800397840

Sd/

Furkan Ahmad

M.SC(Chemistry) 							        13/08/2018

For BMV Fragrances P Ltd				Dated